Kommunikation mit dem Server:

WebPage ← AJAX/JSON → modelbahn-cgi

modelbahn-cgi←UNIX/SOCKET(JSON) → modelbahn-server

Web Interface:

Globale Variablen:

Variable	Where defined
sessionID	serverinout.js	Session ID used for communication with the server. The server will supply this string.

Reservierte HTML Ids:

locodetail	Locomotive detail display

Functions:

locodetail_show(LOCID)	Create and Show Locomotive Setup Display and Load Data from Server / LOCOID – Locomotive to load the Data or keep empty for new LOCO
locodetail_request(REQUEST)	Request Detail Data for the givin locomotive
locodetail_requestcallbac(RESPONSE)	Callbackfunction for the locomtive request
serverinout(REQDATA, CALLBACK(response))	Send Data to the server and callback function for the Response
gWindowCreate(ID, SIZEX, SIZEY)	Create a new Window

JSON Commands:
these commands can be send to the server.

addlocomotive
dellocomotive
setlocomotive	Set Speed or Function of Locomotive, Enabel/Disable Automatic
addsensor
delsensor
setsensor	Enable/Disable Simulation
addinterface
delinterface
addturnout
delturnout
setturnout	Enable/Disable Turnout
poweron
poweroff
reset	Reset All Dynamic Data
save	Save Track to File
status	Get Status
getall	Get all Data (should be send after connect)

Server:

Load/Save Data:

If we load with an empty string we will load from the default location (DEFAULT_DATADIR). Savinging the data will also create the destination folder if it doesn‘t exists.

Static Elements will hold the basic data as locomotives, railways and the controllers to use.

track.json	Railway elements

Dynamic Elements will keep all the dynamics, like turnout status and locomotive assignments.

dynamics.json	Dynamische Elemente